## Slide 1: In-Fiber Network

## Slide 2: Urbana-Chicago Fiber Link
Fiber Loop from UIUCRantoulUIUC
52.6-km roundtrip fiber
~18.5-dB loss at 1550nm

## Slide 3: Polarization Stability
Send different wavelengths utilizing tunable laser
  1549-1550nm
Measure the polarization after sending light of different wavelengths through the loop over multiple hours

## Slide 4: Polarization Stability

## Slide 5: Polarization Stability
Single polarization correction not viable for different wavelengths

## Slide 6: Polarization Check Method 2

## Slide 7: Photon Pair Source
F1=150 mm
F2=200 mm
Signal beam waist 39um
Signal beam waist 2.5mm
F=15.29mm
Pump beam waist 25um
Tsunami
Pulse
shaper
HWP
QWP
Dichroic
DPBS
F1=150 mm
F2=200 mm
F2=200 mm
LP filter
LP filter
PPTKP
DHWP
Aspheric lens/coupling stage
Aspheric lens/coupling stage
Focusing and collimating lens
Cross g2:
Auto g2:
Pump with Tsunami (80 Mhz, 775nm, 100fs )+pulse shaper (With grating+single model fiber as small slit), the shaped pulse is around 0.65nm bandwidth at 1550, but not Fourier transform limited.
The photon are detected with InGaAs detection, with <10% efficacy and 40K/4K dark counts rate

## Slide 8: Photon Pair Source
Expected purity with 1.5ps pump

## Slide 9: Pritel Laser
Mode Locked fiber laser in telecom (tunable around 1550nm)
  Tunable rep rate up to 10.017GHz
Pulse-widths from 1.3-6.5ps
SHG also provided with laser
Possibly use the laser/SHG to pump the single photon source instead of current setup

## Slide 11: Pritel SHG

## Slide 12: PPS Future Measurements
F1=150 mm
F2=200 mm
Signal beam waist 39um
Signal beam waist 2.5mm
F=15.29mm
Pump beam waist 25um
Pump beam waist 1.5mm
Pritel
SHG
HWP
QWP
Dichroic
DPBS
F1=150 mm
F2=200 mm
F2=200 mm
LP filter
LP filter
PPTKP
DHWP
Aspheric lens/coupling stage
Aspheric lens/coupling stage
Focusing and collimating lens
Colin’s SNSPD
Pump with Pritel laser (1560nm, tunable pulse duration)
The photon can be collected and sent to Colin’s SNSPD for a g(2) measurement.
There are currently 12 links between two labs